MOMENTS

The MOMENT of a force is a measure of its capability to rotate the body on which it is acting.

The moment of a force (about an axis through A)   =   F × d

Sometimes, the distance d may need to be calculated

d = x sin θ

Moments are measured in Newton-metres (Nm)

Sense of rotation (clockwise or anticlockwise) must be stated in words or symbols

Examples

1)

O (	Moment  =  7 × 4  =  28 Nm (

2)

A (

Alternatively:

“Split into two perpendicular components”

A(

Ex 5A p 118

SUM OF MOMENTS AFFECTING A BODY

Example

P (

Example

P (

Ex 5B p 121

PLANKS and SEE-SAWS

Example

P(

R(↑)

Example

Q(

R(↑)

Read pp 139-140 including Examples 7 & 8 on Non-Uniform Rods

TILTING

When a rod/plank is on the point of tilting about an axis, it loses contact with any other supports and the reaction at those other supports becomes zero.

Example

A uniform plank of length 3 metres and mass 8 kg rests on two supports A and B.  A is 1 metre from one end of the plank and B is 1 metre from the other end of the plank.  Find the maximum mass that be placed on one end of the plank without the plank tilting.

B(

Ex 5C p 125

NON-UNIFORM BODIES

If a rigid body is non-uniform, you will be told where its centre of mass is or that is what you have to find out.

Example

A non-uniform plank AB of mass 10kg and length 6 metres rest on 2 supports C and D where AC = 2 m and AD = 4 m.  The magnitude of the reaction at C is twice the magnitude of the reaction at D.  Find the distance of the centre of mass from A.

A (

R (↑)

Ex 5D p 128

Mixed Ex 5E p 128

# Text boxes

Moment = Force × Distance of line of action of the force

from the turning point

Notation:

O (  “Taking clockwise moments about [an axis through] O”

Sum of moments